## Slide 1: CEE 111 Engineering Drawing Lecture 2
Sheet layout
Title block
Lettering
Dimensioning

## Slide 2
Sheet Layout
c = 10 mm
d = 25 mm

## Slide 3
Sheet Layout
Border lines
  Perpendicular to each other
  Reference lines
25
10
10
10

## Slide 4
Sheet Layout
Title block
  160 mm X 63 mm
160
63

## Slide 5
Sheet Layout
Title block
  Division in 7 horizontal strips of 9 mm thickness
  Dark lines and lighter lines

## Slide 6
Sheet Layout
Title block
  Division in 7 horizontal strips of 9 mm thickness
  Dark lines and lighter lines
  Leave 4 mm space at the left, then commence writing.

## Slide 7
Title block

## Slide 8
LETTERING
  Writing text on a drawing (e.g. titles, dimensions, scales) using letters which can be alphabets, numerals, symbols or punctuation marks to convey detailed information.
Features of Lettering
Legibility, uniformity, ease, rapidity of execution and reproducibility
No ornamental or artistic and cursive style of letter
Letters should be distinguishable from each other in order to avoid any confusion even in case of slight mutilations
Standard followed
  IS 9609 (Part 0): 2001 & SP46: 2003 (lettering for technical drawings). This BIS standard is based on ISO 3098-0: 1997

## Slide 9
Types of Lettering
  Single stroke - Thickness of the line of the letter should be such as is obtained in one stroke of the pencil.
  Does not mean that the letter should be made in one stroke without lifting the pencil.
BIS (SP46:2003) - Gives dimensions for lettering & types
Type A - Height of capital letter is divided into 14 parts
Type B – Height of capital letter is divided into 10 parts
Both types can be Vertical or Inclined at 75˚ to the horizontal
Line Width of Type A ˂ Type B
Double stroke- When more thickness is given to single stroke letters, it is known as double stroke or gothic letters.
Basic Strokes

## Slide 10
A lettering template

## Slide 11
1
1
2
3
“I” letter
“A” letter
1
2
3
4
5
6
“B” letter
Examples
Height and width of letters
.
Sl. no | Items on a drawing | Size (mm)
1 | Name of the company | 10, 14, 20
2 | Drawing numbers, letters denoting section planes | 10,14
3 | Title of the drawing | 7, 10
4 | Sub- titles & Headings | 5, 7
5 | Dimensioning, notes, schedules & material lists | 3.5, 7
6 | Alteration entries and tolerances | 3.5
BIS (SP 46: 2003) has recommended the heights of letters as: 1.8, 2.5, 3.5, 5, 7, 10, 14 & 20 mm
The height-to-width ratio for letters varies between 7 : 5 or 7 : 6
Total height of lowercase letters equals that of capital letters.

## Slide 12
A & B type
Lettering
BIS (SP46: 2003)
Specifications | Type | Value | Size (mm) |  |  |  |  |  | 
Capital letter height | A | h | 2.5 | 3.5 | 5 | 7 | 10 | 14 | 20
 | B | h | 2.5 | 3.5 | 5 | 7 | 10 | 14 | 20
Lowercase letter height | A | a=(5/7)h | - | 2.5 | 3.5 | 5 | 7 | 10 | 14
 | B | a=(7/10)h | - | 2.5 | 3.5 | 5 | 7 | 10 | 14
Thickness of lines | A | b=(1/14)h | .18 | .25 | .35 | .5 | .7 | 1 | 1.4
 | B | b=(1/10)h | .25 | .35 | .5 | .7 | 1 | 1.4 | 2
Spacing between characters | A | c=(1/7)h | .35 | .5 | .7 | 1 | 1.4 | 2 | 2.8
 | B | c=(1/5)h | .5 | .7 | 1 | 1.4 | 2 | 2.8 | 4
Minimum spacing between words | A | d=(3/7)h | 1.05 | 1.5 | 2.1 | 3 | 4.2 | 6 | 8.4
 | B | d=(3/5)h | 1.5 | 2.1 | 3 | 4.2 | 6 | 8.4 | 12
Minimum spacing between baselines | A | e=(10/7)h | 3.5 | 5 | 7 | 10 | 14 | 20 | 28
 | B | e=(7/5)h | 3.5 | 5 | 7 | 10 | 14 | 20 | 28

## Slide 13
Vertical Capital Letters and Numerical
Vertical Lowercase Letters

## Slide 15
Inclined Capital Letters
At 75˚
Height of numerator and denominator = 3/4th of height of non-fractioned number
Spacing between division bar and numerator or denominator should be such that the total height of fraction will be twice of that of non-fractioned number
Fraction & Indices lettering
The height of index is half of height of a base letter

## Slide 16
Few Tips
If you put the central horizontal strokes of the letters B, E, F, and H at mid-height, they will appear to be below center. To overcome this optical illusion, draw the strokes B, E, F, and H slightly above the center as you letter, keeping letters uniform, as in the second example of fig(right below).
Use extremely light horizontal guidelines to keep letter height uniform as shown in Figure (left above). Do not use vertical guidelines to space the distance from one letter to the next within a word or sentence . This should he done by eye while lettering.
Some combinations, such as LT and VA, may have to be slightly closer than other letters to look correctly spaced. In some cases the width of a letter may be decreased slightly. In typesetting, pairs of letters that need to be spaced more closely to appear correctly are called kerned pairs.

## Slide 17: How to begin your drawing?
Clean the drawing board and all the drawing instruments using duster.
Fix the drawing sheet.
Draw border lines using HB pencil.
Complete the title box using HB pencil.
Plan spacing of drawings b/n two problems/views beforehand.
Print the problem number on the left top and then commence the drawing work.

## Slide 18: Keeping drawing clean – a must
Never sharpen pencils over drawing.
Clean pencil point with a soft cloth after sharpening.
Keep drawing instruments clean.
Rest hands on drawing instruments as much as possible – to avoid smearing the graphite on the drawing.
When darkening lines – try to work from the top of the drawing to the bottom, and from left to the right across the drawing.
Use brush to remove eraser particles. Never use hands.
Always use appropriate drawing pencils.

## Slide 19: Units of Measurement
International systems of units (SI) – which is based on the meter.
Millimeter (mm) - The common SI unit of measure on engineering drawing.
Individual identification of linear units is not required if all dimensions on a drawing are in the same unit (mm).
The drawing shall however contain a note: ALL DIMENSIONS ARE IN MM. (Bottom left corner outside the title box)

## Slide 20: Dimensioning
Indicating on a drawing, the size of the object and other details essential for its construction and function, using lines, numerals, symbols, notes, etc.
Extension line – a thin, solid line perpendicular to a dimension line, indicating which feature is associated with the dimension.
Visible gap – there should be a visible gap of 1.5 mm between the feature’s corners and the end of the extension line.

## Slide 22
Important elements of dimensioning

## Slide 23
Dimensioning
Most convenient unit of length is millimeter.
Angles are shown in degree
  Extension line
  Dimension line
  Leader line
  Arrow heads
  Dimensions

## Slide 24
Dimensioning: Example

## Slide 25
Best practices for dimension & extension lines
The shorter dimensions are nearest to the object outline.
Dimension lines should not cross extension lines as in Figure (b), which results from placing the shorter dimensions outside. Note that it is perfectly satisfactory to cross extension lines (Figure a), but they should not be shortened (Figure c).
Dimension lines should not cross each other & any other lines of the object. However extension lines can cross both (fig 1).
A dimension line should never coincide with or extend from any line of the drawing (Figure d).
Fig 1

## Slide 26
Best practices for dimension & extension lines
Dimensions should be lined up and grouped together as much as possible, as in Figure 2a, and not as in Figure 2b.
In some cases, extension lines and center-lines must cross visible lines of the object (Figure 3a). When this occurs, gaps should not be left in the lines (Figure 3b).
Fig 2
Fig 3
Dimensions should be placed outside the views (a). Placed inside if more clear and readable (b).

## Slide 27
Aligned system | Unidirectional system
Dimensions are placed perpendicular to the dimension line. Horizontal and inclined dimensions can be read from the bottom of the drawing. Vertical dimensions can be read from the right-hand side of the drawing. All dimensions are placed above the midpoint of dimension lines. | Dimensions are placed vertically irrespective of dimension lines. All dimensions can be read from the bottom of the drawing. Horizontal dimensions are placed above the midpoint of dimension lines. Vertical and inclined dimensions are placed at the middle of dimension lines by breaking them.
Systems of dimensioning
For placing the dimensions on the drawing, following systems can be adopted.
All the dimensions on a drawing must be shown using either Aligned System or Unidirectional System. Two systems should not be mixed on the same drawing.
Note

## Slide 28
Chain dimensioning | Parallel dimensioning | Combined dimensioning
All dimensions are aligned in such a way that an arrowhead of one dimension touches tip-to-tip the arrowhead of adjacent dimension. The overall dimension is placed outside the other smaller dimensions. | All dimensions are shown from a common reference line. All dimensions share a common extension line. This is adopted when dimensions have to be established from a particular datum surface. | Both the methods (chain & parallel) are used on the same drawing
 | Used where a number of dimensions have a common datum feature | 
Arrangement of dimensions

## Slide 29
Dimensioning radii
Arcs of Circle Precede with ‘R’ to distinguish from length
Dimensioning of circular features
A circle should be dimensioned by giving its diameter instead of radius. The dimension indicating a diameter should always be preceded by the symbol ø.
Dimensioning of angles

## Slide 30
Center line(axis) itself shall not be used as a dimension line with arrowheads as its ends.
Wrong
Correct

## Slide 31: Thank You